Function Templates
by
Tenneti Venkata Suresh(159231)
Foundation TEG
02/12/13

---
Function Templates
Function Template Definition & Instantiation
Template Argument Deduction
Explicit Template Arguments
Template Explicit Specialization
Overloading Function Templates

---
Macros
int min( int a, int b ) { return a < b ? a : b; }
double min( double a, double b ) { return a < b ? a : b; }
Here the functionality of the functions is pretty same except for the differing date types.
Easy solution is to define a macro
Macro:
#define min(a,b) ((a) < (b) ? (a) : (b))
Refer Macros.cpp
Macros just does the text replacement.

---
Problems with Macros
There is no way for the compiler to verify that the macro parameters are of compatible types.
The macro is expanded without any special type checking.
The a and b parameters are evaluated twice. For example, if either parameter has a postincremented variable, the increment is performed two times.
Because macros are expanded by the preprocessor, compiler error messages will refer to the expanded macro, rather than the macro definition itself.
Also, the macro will show up in expanded form during debugging.

---
Function Template Definition
Function templates provide a mechanism by which we can preserve the semantics of function definitions and function calls.
The function templates does not bypass the C++'s strong type-checking.
The arguments are evaluated only once prior to the invocation of the function
The programmer parameterizes all or a subset of the types in the interface (the parameter and return types) of a function whose body otherwise remains invariant.
Refer program Template1.cpp

---
Function Template Definition
The keyword template always begins both a definition and a declaration of a function template.
The template parameter list follows the keyword template bracketed by <> tokens. It cannot be empty.
When the template is instantiated, an actual built-in or user-defined type is substituted for the template type parameter.
The template nontype parameters are usually constants and are used to specify the sizes of the data containers.
For each set of the template type parameter, a template instantiation is generated.

---
Function Template Definition
A function template can be declared inline or extern in the same way as a nontemplate function. The specifier is to be placed after the template parameter list.
An entity in the global namespace with the same name as that of the template type parameter is hidden. [Refer Template2.cpp]
The C++ standard library provides function templates for commonly used algorithms such as min() defined here. [Refer Template3.cpp]

---
Template Argument Deduction
A function template acts as an abstract structure which needs to be instantiated.
A concrete function definition needs to be constructed and this process is referred to as template instantiation
It occurs implicity either by invoking a function template or taking the address of a function template.
The actual function definition instantiation is determined by the type of the arguments provided on the function call. This is called as template argument deduction.

---
Template Argument Deduction
For template argument deduction to succeed, the type of a function argument need not exactly match the type of the corresponding function parameter.
Following three kinds of type conversions are allowed:
lvalue transformation
qualification conversion [Refer program Template4.cpp]
conversion to a base class instantiated from a class template. [Refer session on Class Templates]
Template argument deduction can fail if the different function arguments resolve to different types [Refer Template5.cpp]

---
Explicit Template Arguments
When the template argument deduction fails, we can explicitly specify the template arguments to be used. [Refer program Template6.Cpp]
When the template arguments are explicitly specified, any implicit type conversion can be applied to convert a function argument to the type of the corresponding function parameter.
We can explicitly specify the template arguments which cannot be deduced from the function call. [Refer prog Template7.cpp]
It is prefered to let the compiler deduce the template arguments rather than providing with an explicit template argument.

---
Template Explicit Specialization
We can provide a specialized definition of the function template to take advantage of the specific knowledge about a type than the one instantiated from the template. [Refer program Template8.cpp]
When a template's explicit specialization is provided, the compiler would use the definition for that template parameter type and would not instantiate for that type.
The explicit specialization must be preceded with the keyword template<> to indicate that it is a specialization, otherwise it is treated as overloading function template.

---
Overloading Function Templates
Type conversions are very limited while deducing the template arguments also in case of the explicit specialization.
Explicit specialization does not help bypass the restrictions on type conversions.
In such cases to gain advantage of the data type conversions provided by the compiler, we can go for overloading the function templates. [Refer program Template9.cpp]